## Slide 1
SMART INDIA HACKATHON 2026
AI-Based Automated Urban Parcel Mapping and Cadastral Feature Extraction System using Drone lmagery
A GeoAI pipeline that converts raw drone imagery into verified, GIS-ready cadastral parcel maps — turning a months-long manual survey into a mostly-automated workflow.
PROBLEM STATEMENT ID
26012
ORGANIZATION
Ministry of Rural Development
DEPARTMENT
Dept. of Land Resources (DoLR)
THEME
Robotics & Drones
Team Solution Pitch

## Slide 2
THE CHALLENGE
Cadastral mapping today is slow, manual, and error-prone
1
Manual digitization
Parcel boundaries traced by hand from drone imagery — slow and inconsistent.
2
Dense, irregular geometry
Overlapping structures, encroachments & narrow lanes confuse manual survey.
3
Delayed land records
Field-based Ground Truthing extends cadastral survey timelines by months.
Bottom line
With ORI, DSM/DTM, and drone datasets now widely available, AI/GeoAI can automate the bulk of feature extraction — leaving humans to verify only the edge cases.
PS 26012 | AI-Based Automated Urban Parcel Mapping & Cadastral Feature Extraction
2

## Slide 3
OUR SOLUTION
A human-in-the-loop GeoAI pipeline for parcel mapping
Drone imagery + elevation data flow through deep learning models to automatically produce validated, GIS-ready cadastral parcels.
1
Ingest & Fuse
ORI + DSM/DTM
aligned & tiled
▶
2
AI Segmentation
Buildings, parcels
& roads extracted
▶
3
Vectorize
Pixel masks →
clean polygons
▶
4
Validate
Topology fix &
conflict flags
▶
5
Review
Web-GIS human
verification
▶
6
Deliver
GIS-ready
cadastral layers
Not fully autonomous by design — every low-confidence or conflicting parcel is routed to a human reviewer before final approval.
PS 26012 | AI-Based Automated Urban Parcel Mapping & Cadastral Feature Extraction
3

## Slide 4
SOLUTION — STAGE 1 & 2
Data fusion and AI-based feature extraction
INPUT DATA FUSED
High-resolution drone imagery
Orthorectified Imagery (ORI)
DSM (surface) + DTM (terrain)
nDSM = DSM − DTM (object height)
Existing GIS parcel layers
GNSS/CORS survey points
Building & Parcel Segmentation
U-Net / Mask R-CNN fine-tuned on Indian urban imagery, using RGB + nDSM as multi-channel input to separate real structures from shadows/clutter.
Output: pixel-level building & parcel masks
Road & Corridor Detection
Lightweight object detection / segmentation head tuned for linear geometry — handled separately from parcels for higher precision.
Output: road & access-corridor vectors
Land-Use Classification
Context features — footprint size, density, proximity to roads — classify each parcel as residential, commercial, mixed-use, or vacant.
Output: land-use tags per parcel
PS 26012 | AI-Based Automated Urban Parcel Mapping & Cadastral Feature Extraction
4

## Slide 5
SOLUTION — STAGE 3 & 4
From pixel masks to validated cadastral polygons
01
Contour Extraction
Trace boundaries of every AI-detected mask into raw polygon outlines.
02
Polygon Simplification
Douglas-Peucker style simplification removes jagged pixel noise.
03
Topology Snapping
Adjacent boundaries snapped together; small gaps auto-closed.
04
Conflict Detection
Overlapping / inconsistent parcels flagged — direct encroachment signal.
WHY THIS MATTERS
Automated topology validation is what makes the output usable in real GIS systems — no self-intersecting polygons, no slivers, no unexplained gaps between adjoining parcels. The same module auto-flags encroachments and boundary conflicts that would otherwise surface only during manual field verification.
PS 26012 | AI-Based Automated Urban Parcel Mapping & Cadastral Feature Extraction
5

## Slide 6
SOLUTION — STAGE 5
Web-GIS dashboard with human-in-the-loop review
● ● ● Cadastral Review Console
⚠ Conflict flagged — needs review
✓
Confidence scoring
Every parcel/building carries a model confidence score.
✓
Smart routing
Only low-confidence or conflicting parcels reach a reviewer.
✓
Accept / reject / redraw
Field officers edit boundaries directly on the map.
✓
GT & GNSS overlay
Ground-truth and CORS survey points shown as reference.
Built on Leaflet/Mapbox + PostGIS — practical for real government deployment, not just a research demo.
PS 26012 | AI-Based Automated Urban Parcel Mapping & Cadastral Feature Extraction
6

## Slide 7
DELIVERABLES
What the platform delivers
1
AI/ML Parcel Extraction Engine
End-to-end segmentation + detection pipeline for parcels, buildings and roads.
2
GIS-Ready Cadastral Outputs
Clean shapefile / GeoJSON exports directly usable in existing GIS systems.
3
Web-Based Visualization Dashboard
Interactive map for review, editing and approval by field officers.
4
Automated Topology Validation
Continuous geometry checks and conflict/encroachment flagging.
↓ Time
Weeks, not months, per ward
↑ Accuracy
Consistent AI + human-verified boundaries
↓ Manual Effort
Reviewers focus only on flagged parcels
PS 26012 | AI-Based Automated Urban Parcel Mapping & Cadastral Feature Extraction
7

## Slide 8
TECHNOLOGY STACK
Built on a proven, deployable stack
AI / Modeling
U-Net, Mask R-CNN, CNN-based object detection; PyTorch / TensorFlow
Geoprocessing
GDAL, Rasterio, Shapely for raster-to-vector & topology ops
Backend & Storage
PostGIS spatial database, REST APIs for GIS data exchange
Frontend / Web-GIS
Leaflet / Mapbox GL for interactive map visualization & editing
PS 26012 | AI-Based Automated Urban Parcel Mapping & Cadastral Feature Extraction
8

## Slide 9
From months of manual survey
to a mostly-automated pipeline.
AI does the heavy lifting. Humans verify only what matters.
Thank You
PS 26012 — AI-Based Automated Urban Parcel Mapping and Cadastral Feature Extraction System using Drone Imagery